## Slide 1
CO1 · MODULE 1 · LAB 1 · CONCEPT 1
The Day-One “SignalDash” Architecture
How does a temperature reading from a physical sensor appear as a live graph inside a web browser?
Duration: 30–40 minutes (Discussion before coding)
Sensor
→
MQTT
→
Node.js
→
WebSocket
→
React
→
Chart.js

## Slide 2
LEARNING OUTCOMES
After this discussion, you will be able to
Understand the complete architecture of the SignalDash application.
Explain how engineering sensor data reaches a web browser.
Identify the role of each software component in the system.
Differentiate between data producers and data consumers.
Understand why modern engineering systems use event-driven communication.
CO1 · Module 1 · Lab 1 — SignalDash Architecture
2

## Slide 3
1. INTRODUCTION
Architecture before code
In many engineering laboratories, students begin programming immediately. Professional software engineers, however, spend considerable time understanding system architecture before writing code.
The SignalDash application is the “North Star” project for this entire course — every lab builds on it, adding new features and capabilities.
Answering the core question requires understanding the complete data journey, end to end, before a single line of code is written.
The Fundamental Question
How does a temperature reading from a physical sensor appear as a live graph inside a web browser?
CO1 · Module 1 · Lab 1 — SignalDash Architecture
3

## Slide 4
2. WHAT IS SIGNALDASH?
A real-time engineering monitoring dashboard
SignalDash displays continuously changing measurements from sensors — instead of refreshing the page repeatedly, the dashboard updates automatically the instant new sensor data becomes available. This is called a real-time monitoring system.
Examples of Monitored Quantities
Temperature
Pressure
Voltage
Current
Humidity
Frequency
Flow Rate
Machine Vibration
Live Reading Feed
Time | Temp (°C)
10:00:01 | 32.4
10:00:02 | 32.5
10:00:03 | 32.7
10:00:04 | 32.6
Every second, a new reading arrives — the sensor itself knows nothing about websites. Its only job is to measure physical quantities.
CO1 · Module 1 · Lab 1 — SignalDash Architecture
4

## Slide 5
3. THE COMPLETE DATA JOURNEY
Five Components, One Continuous Pipeline
1
Physical Sensor
Measures reality
2
MQTT Broker
Post office for data
3
Node.js Backend
The intelligent bridge
4
WebSocket
Persistent connection
5
React Frontend
Reactive rendering
6
Chart.js
Visualizes the trend
Each component has one specific responsibility — modern engineering systems are built by connecting specialized parts, not one monolithic program.

## Slide 6
STEP 1 OF 6
Physical Sensor — The Data Producer
Everything begins with a physical sensor. Its only job is to measure a physical quantity — it knows nothing about websites, browsers, or graphs.
EXAMPLES
Weather station
Temperature sensor
Pressure transmitter
Smart energy meter
Industrial PLC
IoT development board
Discussion Question
Can a sensor display graphs?
Answer: No.
Sensors only generate measurements. Another system is responsible for visualization.
CO1 · Module 1 · Lab 1 — SignalDash Architecture
6

## Slide 7
STEP 2 OF 6
MQTT Broker — The Telemetry Pipe
The sensor cannot send data directly to every application. Instead, it publishes to an MQTT Broker — think of it as a post office: the sensor delivers a message, and anyone interested can receive it.
{
"temperature": 32.4,
"humidity": 71,
"pressure": 1008
}
The broker holds the message only briefly and immediately forwards it to all subscribers.
Why MQTT?
Very lightweight
Minimal network usage
Fast, low-power communication
Works on unreliable networks
Scales to thousands of devices
Why not send sensor data directly to every browser?
Too many users to manage
Poor scalability
Security concerns
High network overhead
CO1 · Module 1 · Lab 1 — SignalDash Architecture
7

## Slide 8
STEP 3 OF 6
Node.js Backend — The Bridge
The backend is the intelligent bridge between engineering devices and web applications. It subscribes to the MQTT Broker and reacts the instant new data arrives.
MQTT Message
Node.js receives it
Processes the data
Sends it to connected browsers
The Backend Also May…
Validate incoming data
Remove incorrect values
Add timestamps
Store data in a database
Generate alerts / calculations
Why Node.js?
Its event-driven, non-blocking architecture responds to events as they occur rather than waiting for one task to finish — ideal for continuous sensor streams and many simultaneous browser connections.
CO1 · Module 1 · Lab 1 — SignalDash Architecture
8

## Slide 9
STEP 4 OF 6
WebSockets — The Persistent Connection
Traditional Request → Response
Browser
Request
Server
Response
This repeats every time new data is needed — continuously refreshing every second is inefficient.
WebSockets Solve This
Browser
Node.js
PERSISTENT CONNECTION
Once established, the browser and server stay continuously connected. New data is pushed to the browser the instant it arrives — no new request needed. This is server push communication.
Used by: stock markets · multiplayer games · industrial dashboards · live monitoring
CO1 · Module 1 · Lab 1 — SignalDash Architecture
9

## Slide 10
STEP 5 OF 6
React Frontend — The Dashboard
The browser receives new sensor values through the WebSocket connection. React automatically updates the user interface whenever new data arrives — no manual refresh required. This is reactive rendering.
OLD TEMPERATURE
32.4°C
New data
arrives
NEW TEMPERATURE
32.5°C
Screen updates automatically
CO1 · Module 1 · Lab 1 — SignalDash Architecture
10

## Slide 11
STEP 6 OF 6
Chart.js — Visualizing the Data
Numbers alone are difficult to interpret. Charts help engineers quickly recognize trends and patterns — rising temperatures, sudden drops, oscillations, or abnormal behavior.
INSTEAD OF READING RAW NUMBERS…
32.4
32.5
32.7
32.8
32.6
…Chart.js draws a continuously updating line graph that reveals the trend at a glance.
Chart: Live Temperature Trend
| t1 | t2 | t3 | t4 | t5
Temperature (°C) | 31.2 | 32.4 | 32.5 | 32.7 | 33.1
CO1 · Module 1 · Lab 1 — SignalDash Architecture
11

## Slide 12
PUTTING EVERYTHING TOGETHER
The Complete SignalDash Workflow
1
Sensor measures temperature
2
Publishes MQTT message
3
MQTT Broker receives data
4
Node.js subscribes to topic
5
Node.js sends data via WebSocket
6
React receives live data
7
Chart.js updates the graph
Every new sensor reading follows the same path — creating a seamless real-time monitoring experience.

## Slide 13
REFERENCE
Key Terms
Sensor
Produces physical measurements
Telemetry
Automatic transmission of measurement data
MQTT
Lightweight messaging protocol for IoT
Broker
Central message distribution service
Publisher
Device that sends data
Subscriber
Application that receives data
Node.js
Backend runtime that processes events
WebSocket
Persistent two-way communication protocol
React
Frontend library for dynamic user interfaces
Chart.js
JavaScript library for interactive charts
CO1 · Module 1 · Lab 1 — SignalDash Architecture
13

## Slide 14
DISCUSSION
Think Like an Engineer
Where does the data originate?
Which component transports the data?
Who processes the data?
How does the browser receive updates instantly?
Why is a real-time architecture preferable to repeatedly refreshing a webpage?
What might happen if the MQTT Broker becomes unavailable?
CO1 · Module 1 · Lab 1 — SignalDash Architecture
14

## Slide 15
LAB PREPARATION ACTIVITY
Trace the Journey
Ask students to trace the journey of a single temperature reading from the sensor to the graph, and identify the responsibility of each component in the architecture.
This reinforces the idea that every technology in SignalDash has a distinct role — modern engineering applications are built by connecting specialized components, not by relying on a single monolithic program. This systems-thinking mindset mirrors industry practice and will make the subsequent lab sessions much easier to follow.